1. Booting Process in Linux (Steps in detail)
Step 1: BIOS / UEFI Initialization
Do you know whether your RHEL 9 system uses BIOS/MBR or UEFI/GPT boot mode?
(You can check using ls /sys/firmware/efi — if that exists, it’s UEFI.)

Step 2: Boot Loader (GRUB2 Stage)
GRUB2 (GRand Unified Bootloader, version 2) is the default bootloader for many
 modern Linux distributions like Ubuntu, Debian, and Fedora. It is the first
 software to run when a computer starts, responsible for loading the operating
 system kernel. GRUB2 can also chain-load other operating systems
and understands various file systems and kernel formats. Key features include UUID support
and a more robust configuration system that uses scripts in /etc/grub.d
 and user settings from /etc/default/grub to generate the final configuration file, /boot/grub/grub.cfg

The Linux kernel is the core, free, and open-source software that acts as the
interface between a computer's hardware and its software. Created by Linus Torvalds
in 1991, it manages crucial system resources like the CPU, memory, and devices,
 enabling different software and applications to run on various hardware.
 It is the central component of Linux-based operating systems used globally.
Key functions of Linux kernel
Hardware abstraction: The kernel provides a consistent interface for software to interact with diverse hardware components, so applications don't need to know the specific details of every device.
Resource management: It handles the allocation and management of system resources,such as the CPU, memory, and input/output (I/O) operations, to ensure smooth and efficient operation.
Process management: It schedules and manages all the processes running on the system, determining which ones get access to the CPU and for how long.
File system management: The kernel manages file systems, providing access to files
and directories while handling storage and permissions.
Device control: It includes and manages device drivers, which allow the operating system to communicate with hardware devices.

 💻 What an Operating System Is:

An Operating System (OS) =Kernel + System Utilities + User Interface + Applications So, when you install Ubuntu, Fedora, or RHEL, you’re actually installing:

The Linux kernel
Plus tools like bash, systemd, coreutils, package managers, etc.
Together, these form a Linux-based Operating System (often called a Linux distribution).
🧩 In short:
Term	Description
Linux Kernel	The core that controls hardware and resources
Linux OS / Distro	Kernel + user tools + UI = complete system
Example:
Kernel → “Engine”
Linux OS → “Car” 🚗 (engine + body + wheels + controls)

Initramfs
when the linux kernal is first booted it doesnot have access to
 the real file systems ans it needs drivers(ext4,xfs,LVM) for the disk control,
drivers are in disk. therefore the along with the linux kernal
the bootloader loads the initramfs, where the initial ram file systemacts as a small linux system
it has the basic tools, drivers, scripts.
Bootloader → loads the Linux kernel and the initramfs into memory (RAM)
✅ The bootloader’s job is to copy both files (vmlinuz and initramfs.img) from disk into RAM.
Linux kernel → uses the initramfs
✅ Once the kernel is running (already in memory), it extracts and mounts the initramfs as a temporary root filesystem.

where does kernel gets init?------root filesystem.
The kernel gets init from either the init= parameter (if specified) or the default path /sbin/init on the root filesystem.
        but
u saying init is in rootfile system in third step we only mounted the intramfs how kernel acces init if it is in root file system

1️⃣ After the kernel loads, the only filesystem it can see is the initramfs — a small temporary root filesystem built into memory.

This initramfs is loaded by GRUB alongside the kernel (the file is something like /boot/initramfs-<version>.img).

It contains a minimal Linux environment with a few programs, including its own /init script or binary.

2️⃣ Kernel runs /init inside initramfs first.

This /init is not the final systemd yet.

It’s a small script or binary whose job is to:

Load needed drivers (for disks, LVM, RAID, etc.).

Find and mount the real root filesystem (e.g., /dev/sda2 or /dev/mapper/rhel-root).

3️⃣ Once the real root is ready, that /init inside initramfs does a switch_root (or pivot_root) — this replaces the temporary root with the real one.

4️⃣ Now the kernel can finally see /sbin/init (→ systemd) from the real root filesystem — and executes it as PID 1.

💬 So, in order:

GRUB → Kernel → /init (from initramfs) → switch_root → /sbin/init (systemd)

✅ In short:
The kernel first runs /init from initramfs (in RAM), which mounts the real root filesystem and then starts /sbin/init (systemd) from there.

### 🖥️ What is TTY?
TTY stands for Teletypewriter — an old word from when people used physical terminals to talk to big computers.
In Linux, it now means a text-based terminal (no GUI).

### 🔍 In modern Linux:
- Each virtual console (Ctrl + Alt + F1 to F6) is a TTY — for example:
  - tty1, tty2, tty3, etc.
- Each one gives you a login prompt you can type in.
- The GUI (like GNOME) runs on tty1 or tty7 depending on your system.

### 🧠 Commands:
- Check which terminal you’re on:
  tty
  → Output might be /dev/tty2 or /dev/pts/0.
- /dev/tty = current terminal device file.

💬 In short:
A TTY is a text-based login screen or virtual console that lets you interact directly with the system.

What is bash?
Bash can refer to the Bourne Again Shell, a command-line interpreter and scripting language for Unix-like operating systems

what is PAM (Pluggable Authentication Modules)
🧍‍♂️ Step 6: Login and Shell Initialization
 ------User logs in:
You type your username + password.
Pluggable Authentication Modules (PAM) is a framework that provides a flexible and extensible way to manage user authentication and other security-related tasks on a system. It allows system administrators to integrate various authentication mechanisms and security policies without modifying the underlying applications.